## Slide 1: Firefly Luciferase Quantification Assay
Kostandino Koci
November 2022

## Slide 2: Background
LNP-mediated delivery of mRNA towards specific cells is the current platform we are deeply interested in for effective targeted therapeutics
When delivered, the mRNA utilizes cytosolic ribosomes to translate and produce a therapeutic biomolecule
To test the efficiency of the mRNA delivery and translation, we will deliver firefly luciferase(fLUC) mRNA via LNPs intravenously (IV) and perform quantification assays on the product
We selected fLUC as it is not endogenous to the system and it can be easily induced to luminesce

## Slide 3: Assay Goals
We will perform a full panel analysis of fLUC for the site of injection muscle, plasma, liver, kidney, heart, and brain
Each organ will be homogenized and lysed, then centrifuged for supernatant
fLUC mRNA and protein will be quantified to determine concentration
Results will be recorded and delivered in meetings

## Slide 4: Issues
Unlike our previous biomarker assays, we cannot procure fLUC quantification kits as they are not available
The current body of literature does not have an established fLUC quantification assay
Developing immunoassays like ELISA or Western-Blot cannot be performed due to the lack of available commercial monoclonal or polyclonal antibodies
The best available product is the Promega fLUC luminescence assay. However:
  The assay only works for cell lines
  And to perform the assay, we would need to purchase the Promega plat reader
Our best bet is to perform the assay in-house

## Slide 5: Developing the Assay
Our main approach will be an ELISA-style induced luminescence assay, where we will quantify the firefly luciferase based on a standard curve
  We can purchase fLUC commercially to help us build controls and a standard curve
There are a few elements that can help us develop this assay in-house:
  Our current plate reading templates and procedures in Excel are already optimized for fitting the standard curve
  Promega kits do provide resuspended luciferin protein, which will activate fLUC and induce luminescence
  The Variosakan-LUX plate reader can be modified to not just record luminescence in dark conditions(optimal for FLUC) but also dispense the resuspended Promega luciferin solution via dispensers, which we can procure and easily install
  In addition, the Variosakan-LUX manual does provide detailed methods for how we can effectively dispense

## Slide 6: Developing the Assay
Since our main target is luminescence, we are going to focus on two elements
  Determine optimal luminescence recording conditions
  Develop a standard curve and controls for fLUC
We determined that the optimal way of inducing luminescence via the fLUC and luciferin nitration would be to add equal parts in a 96-well plate
  The plate cannot be translucent, or we risk luminescence crossing over
  Solid plastic white or black plates do not seem to be different in measurements
Samples of the same group must be pooled and tested with various dilutions
  This is to determine the level of sensitivity we need to employ
The optimal volume seems to be about 50 μL for recording
  We decided that we can achieve this with 25 μL of tissue homogenate/plasma and 25 μL of resuspended luciferin
  Therefore, we must account for the 1:2 dilution as well

## Slide 7: Developing the Standard Curve
Our standard curve needs to be a reflection of the level of sensitivity that we can achieve
  We started out with a standard curve of: 250, 125, 75, 25, 10,0 μg/mL
  This curve was a success in detection, so we decided to lower our sensitivity to about 10ng/mL, allowing us to achieve a dynamic sensitivity range
  The ultimate standard curve we settled was: 250,125,62.5,31.25,15.625,7.813, 0 ng/mL
  Controls were planned to be 50ng/mL and 25ng/mL and must be done by diluting the stock with untreated tissue homogenate
Once we established a standard curve for use, we optimized the process by using a stock of 1 μg/mL fLUC, for which we performed a 1:4 dilution for the curve
  Stock was saved in 2-8*C for short term and -20*C for long term storages

## Slide 8: Results
The standard curve and controls, alongside mock samples diluted with homogenate, seem to indicate that the assay and record luminescence
Testing with samples did yield some level of record; however, the fLUC only seems to be measurable in samples that have a significant concentration
Samples with lower concentrations are more complex to measure, and our assay lacks the sensitivity to measure the concentrations in the pg/mL range
Overall, the assay seems to help detect and measure fLUC concentrations in samples with high translation efficiency
However, further work and literature reviews on recent studies must be performed to be able to extend our sensitivity ranges